## Slide 1: Network planning and design
Diseño y planeación de redes
Ingeniería en Telecomunicaciones

## Slide 2: Contents
Introduction
Network planning
Traffic forecasts
Dimensioning
Ref. : A. Olsson, ed. (1997)
A. Girard (1990)

## Slide 3: Telecommunication network
A simple model of a
telecommunication network
consists of
– nodes
• terminals
• network nodes
– links between nodes
• Access network
– connects the terminals to the network nodes
• Trunk network
– connects the network nodes to each other

## Slide 4: Why network planning and dimensioning?
• “The purpose of dimensioning of a telecommunications network is to ensure that
the expected needs will be met in an economical way
both for subscribers and operators”

## Slide 5: Network planning and design
Network planning and design is an iterative process, encompassing topological design, network-synthesis, and network-realization, and is aimed at ensuring that a new telecommunications network or service meets the needs of the subscriber and operator.
The process can be tailored according to each new network or service.

## Slide 6: A network planning methodology
A traditional network planning methodology in the context of business decisions involves five layers of planning:
Business plan: need assessment and resource assessment
Short-term network planning
IT resource
Long-term and medium-term network planning
Operations, management and maintenance

## Slide 7: A network planning methodology

## Slide 8: A network planning methodology
Each of these layers incorporates plans for different time horizons:
The business planning layer determines the planning that the operator must perform to ensure that the network will perform as required for its intended life-span.
The Operations and Maintenance layer, however, examines how the network will run on a day-to-day basis.

## Slide 9: Traditional planning process
• Traffic aspects
– Data collection (current status)
• traffic measurements
• subscriber amounts and distribution
– Forecasting
• service scenarios
• traffic volumes and profiles
• Economical aspects
• Technical aspects
• Network optimisation and dimensioning
– hierarchical structure and topology
– traffic routing and dimensioning
– circuit routing.

## Slide 10: Traditional planning process
• As with any decision process, network planning relies on external information:
– Forecast of demand for services over some planning horizon
– Economic information concerning the cost structure of the network elements and maintenance
– Knowledge about the technical capabilities of the available systems
• The planning problem can now be stated as follows:
– to implement the first four layers of the OSI model
– to provide the required physical support
• Assuming that all the protocol issues have been settled and the transmission technology is known, what remains is a complex, distributed and dynamic capacity-augmentation problem
– only feasible solution approach: decomposition and iteration

## Slide 11: Traditional planning process
Stages of the planning process:
– Topological design
– Network-synthesis problem
• Traffic routing
• Dimensioning
– Network-realization (circuit-routing) problem
These four stages are interrelated
The planning process is iterative (at many levels)
Different planning horizons at various stages

## Slide 12: Traditional planning process

## Slide 13: Traditional planning process
Topological design:
– Determine where to place components and how to interconnect them
– By methods of topological optimization and graph theory
– Input:
• information about transmission network summarized into a fixed interconnection cost per unit length between offices
• switch costs depending just on the switching technology
– Output:
• connectivity matrix
• optimal location of switches or concentrators (optionally)

## Slide 14: Traditional planning process
Network synthesis:
– Calculate the optimal size of the components (that is: the transmission and switching systems) within the topology specified and subject to GoS constraints on network-performance measures
– By methods of nonlinear optimization
– Input:
• topology, traffic matrices, GoS constraints, cost function (unit cost)
– Output:
• route plan
• set of logical links between the nodes
(that is: requirements for transmission facilities between switching points)
– Comprises of two iterated substages:
• Traffic routing
• Dimensioning
– Specific to telecommunications!

## Slide 15: Traditional planning process
Network synthesis
• Traffic routing:
– Determine how to connect calls as they arrive, given the topology and size of the components.
• Dimensioning:
– Determine the size of the components subject to GoS constraints and given the topology and a routing method.

## Slide 16: Traditional planning process
Network realization:
– Determine how to implement the capacity requirement (for transmission and switching equipments) using the available components and taking further into account reliability (multipath routing)
– By methods of multicommodity flow optimization
– Input:
• logical-circuit demand
• fixed costs, module costs and reliability of available components
• other reliability requirements
– Output:
• physical circuits plan
• detailed information of actual transmission cost between nodes

## Slide 17: New planning process
Additional decision data are needed from the following areas:
– The market, with regard to a specific business concept
• due to competition!
• operator’s future role (niche): dominance/co-operation
– Customer demands:
• new services: Internet & mobility (first of all)
• new business opportunities
– Technology:
• new technology: ATM, xDSL, GSM, CDMA, WDM, ….NGN
– Standards:
• new standards issued continuously
– Operations and network planning support:
• new computer-aided means
– Costs:
• trends: equipment costs going down, staff costs going up

## Slide 18: New planning process
Safeguards for the operator:
– Change the network architecture so that it will be more open, with generic platforms, if possible
– Build the network with a certain prognosticated overcapacity (redundancy) in generic parts where the marginal costs are low
New planning situation (shift of focus to a strategic-tactical approach):

## Slide 19: New planning process
MPLS
FTTH
GPON
Ethernet
SDWAN
Plataformas

## Slide 20: Traffic forecasting Need for traffic measurements and forecasts
• To properly dimension the network we need to
• If the network is already operating,
– the current traffic is most precisely estimated by making traffic measurements
• Otherwise, the estimation should be based on other information, e.g.
– estimations on characteristic traffic generated by a subscriber
– estimations on the number of subscribers
• Long time-span of network investments 
– it is not enough to estimate only the current traffic
– forecasts of future traffic are also needed

## Slide 21: Traffic forecasting
• Information about future demands for telecommunications
– an estimation of future tendency or direction
• Purpose
– provide a basis for decisions on investments in network
• Forecast periods
– time aspect important (reliability)
– need for forecast periods of different lengths

## Slide 22: Forecasting procedure

## Slide 23: Traffic forecast
• Traffic forecast defines
– the estimated traffic growth in the network over the planning period
• Starting point:
– current traffic volume during busy hour (measured/estimated)
• Other affecting factors:
– changes in the number of subscribers
– change in traffic per subscriber (characteristic traffic)
• Final result (that is, the forecast):
– traffic matrix describing the traffic interest between exchanges (traffic areas)

## Slide 24: Traffic matrix
• The final result of the traffic forecast is given by a traffic matrix
• Traffic matrix T = (T(i,j))
– describes traffic interest between exchanges
– N2 elements (N = nr of exchanges)
– element T(i,i) tells the estimated traffic within exchange i
– element T(i,j) tells the estimated traffic from exchange i to exchange j
• Problem:
– easily grows too big: 600 exchanges  360,000 elements!
• Solution: hierarchical representation
– higher level: traffic between traffic areas
– lower level: traffic between exchanges within one traffic area

## Slide 25: Traffic matrix
• The final result of the traffic forecast is given by a traffic matrix
• Traffic matrix T = (T(i,j))
– describes traffic interest between exchanges
– N2 elements (N = nr of exchanges)
– element T(i,i) tells the estimated traffic within exchange i
– element T(i,j) tells the estimated traffic from exchange i to exchange j
• Problem:
– easily grows too big: 600 exchanges  360,000 elements!
• Solution: hierarchical representation
– higher level: traffic between traffic areas
– lower level: traffic between exchanges within one traffic area

## Slide 26: Traffic forecast Example 1
• Data:
– There are 1000 private subscribers and 10 companies with their own PBX’s in the area of a local exchange.
– The characteristic traffic generated by a private subscriber and a company are estimated to be 0.025 erlang and 0.200 erlang, respectively.
• Questions:
– What is the total traffic intensity a generated by all these subscribers?
– What is the call arrival rate l assumed that the mean holding time is 3 minutes?
• Answers:

## Slide 27: Traffic forecast Example 2
• Data:
- In a 5-year forecasting period the number of new subscribers is estimated to grow linearly with rate 100 subscribers/year.
– The characteristic traffic generated by a private subscriber is assumed to grow to value 0.040 erlang.
– The total nr of companies with their own PBX is estimated to be 20 at the end of the forecasting period.
• Questions:
– What is the estimated total traffic intensity a at the end of the forecasting period?
• Answers:

## Slide 28: Traffic forecast Example 3

## Slide 29: Traffic dimensioning
• Telecommunications system from the traffic point of view:
• Basic task in traffic dimensioning:

## Slide 30: Traffic dimensioning
• Observation:
– Traffic is varying in time
• General rule:
– Dimensioning should be based on peak traffic not on average traffic
• However,
– Revenues are based on average traffic
• For dimensioning (of telephone networks), peak traffic is defined via the concept of busy hour:

## Slide 31: Telephone network model Traffic process
• Traffic process in each network node
– due to call establishments
– during the call establishment phase
• each call needs (and competes for) processing resources in each network node (switch) along its route
– it typically takes some seconds (during which the call is processed in the switches, say, some milliseconds)
• Traffic process in each link
– due to information transfer
– during the information transfer phase
• each call occupies one channel on each link along its route
– information transfer lasts as long as one of the participants disconnects
• ordinary telephone calls typically hold some minutes
• Note: totally different time scales of the two processes

## Slide 32: Telephone network model Traffic process
• Traffic process in each network node
– due to call establishments
– during the call establishment phase
• each call needs (and competes for) processing resources in each network node (switch) along its route
– it typically takes some seconds (during which the call is processed in the switches, say, some milliseconds)
• Traffic process in each link
– due to information transfer
– during the information transfer phase
• each call occupies one channel on each link along its route
– information transfer lasts as long as one of the participants disconnects
• ordinary telephone calls typically hold some minutes
• Note: totally different time scales of the two processes

## Slide 33: Telephone network model Traffic dimensioning
• Assume
– fixed topology and routing
– given traffic matrix
– given GoS requirements
• Dimensioning of network nodes:
Determine the required call handling capacity:
– max number of call establishments the node can handle in a time unit
• Dimensioning of links:
Determine the required number of channels:
– max number of ongoing calls on the link