## Slide 1: TELECOM Network planning
Diseño y planeación de redes

## Slide 2: Network planning
Network planning activities evolve with the proper evolution of the network, the services, the technologies, the market and the regulatory environment.
Network planning addresses all the activities related to the definition of the network evolution in order to allow the transport of an expected amount of traffic demands, taking into account a set of requirements and constraints.
For general feasibility -- to economically justify the move towards the evolving architectures --

## Slide 3: Requirements to the planners
o Business Oriented Needs
What are the best customer segments to address in multimedia?
Which new services have to be introduced through time?
What is the best service bundling per customer type?
How to increase market share?
How to maximize revenues?
How to reduce capital expenditure?
How to reduce operational expenditure?

## Slide 4: Requirements to the planners
o Network Oriented Needs
How to forecast multimedia services and related traffic demands?
How many nodes to install, especially for NGN?
What is best location for new systems and related communication media?
What is the best network architecture and routing in NGN?
Best balance between built and lease for infrastructure?
How to plan capacity evolution and solutions migration towards NGN and towards 4G, 5G.
How to converge service applications and platforms through different access technologies?
How to ensure SLA and protection level?

## Slide 5: Requirements to the planners
o Operation Support Needs
How to evaluate alternatives for direct operation and outsourcing?
How to organize and engineer the new operation processes?
Which IT applications ensure an efficient support to operation?
How to train labor force on the new operational activities?

## Slide 6: Typical network planning tasks
Initial situation analysis for economy, customers, services and network
Problem partitioning
Data gathering
Definition of alternatives per scenario
Mapping solutions per scenario
Design, dimensioning, location and costing
Optimization
Sensitivity analysis to uncertain variables
Plan selection and consolidation
Reporting

## Slide 7: Network planning processes

## Slide 8: Network planning processes
New planning process:
Data on topologies, architectures, location, routing, etc from long term planning are transferred to the medium term and iteratively to short term activities
Planning results are transferred to NM applications and vice versa, NM measurements and status are provided as inputs to the planning activities
Operating System Processes also provide data to the short/medium term planning activities on the traffic demand, performance and origin/destination flows.

## Slide 9: Network planning processes Iterative Planning Sub-Processes for Competition Scenarios

## Slide 10: Network planning processes Iterative Planning Sub-Processes for Competition Scenarios
Telecom network scenarios are generated with the premises derived from realistic market share and competitive situation.
Final objective is to have a quantified design fulfilling the strategy for the operator the requirements of the society and being feasible from the business point of view.
Defined processes and tasks are needed for all solutions and technologies. Internal data and algorithms vary for each technology case.
Feedback among activities is needed to incorporate results of the optimization on the inputs and assumptions.
Business assessment is made at the start of the process to select feasible solutions and discard the ones not being realistic.
A more detailed business plan is obtained at the end of the analysis for the selected solutions and providing the business and investment plans.

## Slide 11: planning activities
·Long-term planning (LTP).
Defines and dimension the network parts which are characterised by a long lifetime and large investments for their deployment.
·Medium-term planning (MTP).
The framework should emphasise the behaviour and the relationships among the sets of entities (nodes, links, subnetworks) and the list of planning actions and procedures which are involved when planning a network to guarantee the convergence towards the established long term plans.
MTP has as an objective the capacity upgrading of the network nodes and links; always, following the long-term (LT) deployment strategies of the optical network.
·Short Term Planning (STP).
Determines the routes and the telecommunications systems that support a demand.
The network has to satisfy the current telecommunications demands with the already installed capacities without additional capital investments.

## Slide 12: Long-term planning
Strategic planning
Defining the technology and architecture to be used in the network through the comparison of different options.
It is generally based on a green-field approach and uses parametric models and typical values for the relevant network parameters.
Fundamental planning
Uses as input the technology and network architecture selected by the strategic planning and defines the structure of the network.
Problems: allocation of functions in the network nodes, the topology planning, the apportionment of functions between the optical and the client layer, the definition of an optimal network structure

## Slide 13: Long-term planning
* En muchas disciplinas, un proyecto "greenfield" es aquel que carece de limitaciones impuestas por trabajos anteriores.

## Slide 14: Long-term planning
Dealing with LTP the focus of the project has been on the fundamental planning.
LTP => fundamental planning
LTP defines the following aspects:
Location and technological evolution of the network nodes.
Partitioning into subnetworks (domain definition).
The hub nodes for interconnecting the different domains should be identified.
The hierarchy between the different domains, if any, should be established.
Logical network structure for the considered network layer.
Eventually a mapping of the telecommunications systems on the physical telecommunications infrastructures can be given.

## Slide 15: medium-term planning
The objective of Medium-Term Planning (MTP) is the capacity upgrading of the network nodes and links following the long-term deployment strategies of the optical network.
The goal of the MTP is to determine the routing map and node capacities.
MTP is normally performed in a multi-period basis; setting of the different steps for moving from the installed plan (if any) to the long-term network objective.

## Slide 16: medium-term planning
Results for each planning period:
Detailed routing and grooming for each demand (traffic relation). It should not have conflicts with the defined LTP criteria.
Telecommunications systems to be installed or uninstalled in all the periods. It should be done according to the MT forecasts and inside the set of nodes and telecommunications infrastructure supplied by LTP.
Equipment to be installed, upgraded or uninstalled in all the periods. It should be done according to the MT forecasts and inside the set of nodes defined by the LTP.
Scaling and possible delays in deploying/installing new network elements according to the budget constraints.

## Slide 17: medium-term planning
Inputs for each planning period:
Network nodes (from LTP).
Present and potential fibre routes (from LTP).
Telecommunications systems in use.
Installed equipment in each node.
Forecasted demands for each planning period.
Component costs. It should take into account, installation, upgrading and uninstallation costs of the different systems.

## Slide 18: medium-term planning

## Slide 19: The breakdown approach for LTP and MTP solving
Dividing a problem into simpler sub-problems is recognised as an effective solution for very complex problems like the telecommunications network planning.
Breakdown approach in LTP:
The LTP for telecommunications networks is a very complex problem due to the size and complexity of the realistic network planning tasks.
The division of the overall planning problem in smaller sub-problems (called breakdown approach) decreases the complexity of the planning activity and it has many positive consequences like simpler solution algorithms, shorter development periods, software re-usability,

## Slide 20: The breakdown approach for LTP and MTP solving
Breakdown approach in MTP:
MTP for telecommunications networks is even more complicated than LTP.  First of all that is due to the additional outputs required to MTP
A general methodology to solve a planning problem in the MTP perspective consists in dividing MTP into two separated and related parts: single-period and multi-period.
Single-period planning process objective is to determine quantity and cost of network resources to meet a single-period incremental demand forecast.
Multi-period planning process and its relationships with single-period planning process can be viewed in Figure

## Slide 21: The breakdown approach for LTP and MTP solving
Single-period process in MTP

## Slide 22: The breakdown approach for LTP and MTP solving
Multi-period process in MTP

## Slide 23: Overall plans per network layer and technology
The inherent layering structure of the network and related technologies
together with the complexity of the overall network implies that the
network planning has to be performed also by layers, subnetworks and
technologies:
By Layers in a vertical dimension following the client-server relation (one layer is supported in the layer below and provides resources for the layer up) as indicated: Physical, Transmission, Routing/Switching, and Applications/Services/Control.
By Segments or splitting of the end to end communication into sub areas as customer premises, access, core national, core international.
By Technologies or underlying technique as FO, WDM, PDH, SDH, PSTN, ATM, IP, NGN, 3G, 4G, 5G, etc.....

## Slide 24: Network Layer Modeling for Planning and Design

## Slide 25: Phases of The planning process related to Network Layers

## Slide 26: Solution mapping per scenario
Due to the large variety of geo-scenarios defined by the combination of customers, services, geo-models, density, consumption, available solutions, etc. the planner has to analyze and decide which solution is going to be planned in more detail per scenario type.
The recommended methodology is structured in the diagram with a first selection by technical compliance followed by an economical evaluation of the Cost Of Ownership that is self-explanatory.

## Slide 27: Methodology to obtain best techno-economical solutions per scenario

## Slide 28: Relation among technical, business and operational plans
The number of scenarios and high interrelation among decisions at each level of the organization: Financial, Technical and Operation requires implementing carefully an integrated processing for the information at each Stage.
The large ranges of variation in many cases and the need to optimize synergies in competition obliges to interchange results between the processes and have an Information System across the organization based on Operational Support Systems (OSS) to facilitate consistency and speed of application.

## Slide 29: Relation among technical, business and operational plans
OSS: Operations Support Systems

## Slide 30: Economical modelling and business plans
A Business Plan presents the calculation of the financial indicators that enable the managers to evaluate the financial performances of an enterprise in order to take best decisions for the overall operation.
Due to the high number of alternatives today and the need to find economical feasibility in competition, the business evaluations are being used not only for the business plan itself but as an iterative evaluation of those techno-economical alternatives to select the ones that perform better in the competitive market.

## Slide 31: business plan
A Business Plan summarises the results of the planning process:
the objectives to reach ( subscribers demand, sales)
the future revenues expected from the plan and per service class;
the planned expenses (investment and operations) as overall and per service class;
the accounting statements and the financial indicators characterising the profitability of the project

## Slide 32: Business model structure for planning

## Slide 33: Economic modelling for planning
Economical modelling to evaluate network solutions:
modelling tariffs,
equipment costs per type,
economy of scale,
lifecycle,
equipment deployment,
elasticity,
trends with time

## Slide 34: Economic concepts and terms
Amortisation
Assets
Breakeven period
Capacity Maximum capacity
Nominal capacity
Operational occupancy
Capex- Capital expenditures
Cash Flow
Churn (Churn Rate o Tasa de Abandono)
Depreciation
Discounted Cash Flows
Discount factor
EBITDA (Earnings Before Interest Taxes Depreciation and Amortization)
EVA (Economic Value Agreggated)
Future Value (FV)
Internal rate of return (IRR)
Life cycle costing
Net Present Value (NPV)
Opex
Payback period
Present Value (PV)
Profit: Net Income or Earnings
Residual value
Revenues
ROCE (Return On Capital Employed)

## Slide 35: Main Inflows and Outflows contributing to the cash flow generation

## Slide 36: Economic modelling for services
The service related modelling is a subset of the overall NGN economic modelling that represents with less detail the analysis of technological variants and for a given network solution models with more detail the demand, dimensioning, tariffs, revenues and profitability of the services themselves.
Service impacts on the network and business:
- the overall operation company
- the global network solution
- the broadband platform needed for all new services
- the specific platform for each service type

## Slide 37: Economic modelling for services
Modelling and differentiation of resources, cost drivers, revenue drivers with the corresponding cost allocation per service type is a must for the knowledge of impact from each service and to decide the introduction strategy per service or service bundle:
Major cost drivers for multimedia service require the evaluation of all dimensioning
Those units, dimensioning and costing has to be performed for the network resources
Major revenue drivers for multimedia services need to consider the contract fee, monthly fee and usage/traffic dependent fee, either in erlangs, Mbs, time, delivery unit.

## Slide 38: Cycle life amortization versus modernization
Examples of deployment scenarios over time

## Slide 39: Referencias
ITU. Telecom Network Planning for evolving Network Architectures. Reference Manual. Part 1.
ITU. Telecom Network Planning for evolving Network Architectures. Reference Manual. Part 2.